Turnigy GTX3 – FlySky GT3B

Differences / Improvements

Expo on the GTX3 works correctly.

Ball bearing steering on the GTX3.

Low voltage alarm at 9.1V on the GTX3 (9.4V on the GT3B).

Removing the GTX3 top cover requires removing ALL screws. Carefully unfold the side covers and pull them down. Now that you have access to the PCB you will notice there are even more screws that connect the PCB with the top cover. Remove these plus the select wheel and you have full access to the LCD and PCB.

Gaining access to the steering wheel assembly requires to unscrew it from the inside.