433 Telemetry upgrade

Ground telemetry station has a high level of local noise - 80dB in my case, which decrease range significantly. To improve that I purchased spare 433 Air unit from RC Timer and Hobbyking FeiYu Tech programing cable which is USB to RS232 TTL converter. I connected them together with supplied cables and spare 4 pins. The connection is straigh forward as it needs connect the same color wire to same color wire (with the exeption of white which is connected to yellow).  Wires needs to be removed on one of the connectors and the put them back in correct order as they did not match in default.

Then install the win driver for the cable - inluded in files tab, set the telemetry unit to match the existing air unit (including ID number) and enjoy the greater range.

After this modification the local noise level dropped down to 40 dB which is great value.

Obrázek 1 - Telemetry noise before mod

Obrázek 2 - Telemetry noise after mod