This  action is very necessary, for all motors to run with the same speed and for having a stable flight.

- Make sure that the quadcopter is OFF.

- Turn on the transmitter.

- Turn on the quadcopter to let the Radio receiver and Radio transmitter to know each other.

- Turn OFF the Quadcopter.

- take Throttle to the maximum on radio transmitter.

- Turn on the Quadcopter and wait till you hear a single beep from ESC's.

- take throttle to its minimum and wait till you hear 2 short beeps followed by a single long beep from ESc's.

- Turn off the Quadcopter and turn it on.

- ESC calibration is DONE.

- Make sure to Set the FAILSAFE before flight.

- Quadcopter is ready to fly.

ESC calibration is necessary for APM 2.7 (HK Mega pilot 2.7) but it seems that DJI NAZA does not need to have ESC Calibration!